## Slide 1: Bootloader-r2

## Slide 2: Build process (prepping image)
Linker
Objdump (existing) converts to binary form to be loaded
Binary of image for flash
.elf
Post processor (new) (adds signature to be checked by boot loader)
Image to be loaded
Dfu prep (adds a little extra info needed for DFU processing)
.dfu file

## Slide 3: Abstract boot loader
SPI flash a database of images and other things
There’s some stuff to make sure the bootloader trusts the images. Then bootloader considers the images.
Bootloader needs to make a decision what to do
  What’s in program flash,
  What’s in spi flash, (maybe multiple image)
  Is there any administrative info?
Options
  Copy image X to program flash, then start program flash (if program flash matches inbound image, just start program flash)
  Do nothing and start program flash
  (Discover a problem and copy a safe image from SPI flash to program flash)
  Do nothing and go to safe state
How does bootloader know which image is desired? Possibilities are endless, but perhaps:
  SPI flash (special record that says “this one” – or look for the most recent version, etc.); or
  EEPROM in the CPU has an indication of what to load
  FRAM had an indication of what to load.
Easiest thing to describe is something in EEPROM that specifies the GUID of the image to run. Then the bootloader enforces the invariant that the application image in nor flash is the “best available” image of the images available before starting.

## Slide 4: Initial repo
git@gitlab-x.mcci.com:tmm/bootloader.git
This has a skeletal bootloader, plus some public-domain crypto code “tweetnacl” that can do signature checks.