## Slide 1: Boot Loader for MCCI LoRaWAN systems

## Slide 2: Participating
ChaeHee, Dhinesh, Prabin, Terry, Vel

## Slide 3: Agenda
Requirements
  Implementation
  Test
Scenarios

## Slide 4: Do we want to have “recovery images”?
We don’t have enough room in the boot loader to do much
We might want to have “double reset” load a recovery image from SPI flash
  This could enable USB download, etc. But not great for field use because someone might maliciously do this.
  Maybe an option? Getting complicated! But suggests we want multiple images in the SPI flash beyond the “current/new”. Which suggests “naming”…. Which gets perilously close to a “file system”.

## Slide 5: Observations
There are a lot of corner cases that occur infrequently in practice
  Flash programming failures (occur normally at end of life of product, if at all)
  Power failures during programming
  Brown-out during programming causing strange things to happen
  Power supply spikes or glitches during programming
  Data corruption during transfer
We can’t require that we recover from any problem – there’s no recovery from a persistent flash programming failure
  But we want to recover from non-persistent failures.

## Slide 6: More observations
We only have a small amount of flash available to reserve for the boot loader (8k bytes or less)
  So we have to minimize the amount of work to be done in the boot loader
We want to arrange things so that the boot loader doesn’t have to deal with too many errors. (Push as much error handling as possible outside the boot loader.)

## Slide 7: What should our boot loader do?
Assume:
  We have a primary image in main flash
  We have one or more backup images in bulk storage (“spi flash” in the case of current systems)
Generally:
  If the current image in main flash is corrupt, load the “best image” from bulk storage.
  If the current image in main flash is OK, see if the bulk-storage image is better than the current image. If so, load the image from bulk storage.
Once we have a verified, accepted image in main flash, transfer control to the main image.

## Slide 8: How do we determine if main flash is valid?
Normal method: do a signature (CRC or cryptographic) to confirm that the image is valid.
There is CRC32 hardware in the STM32 for this purpose.
This begs the question: what area of flash gets checksummed? Not the boot loader itself, because the boot loader is a separate program.
  We might separately check boot loader itself, and decide to just fail (blink light) if boot loader is corrupt.
This begs the question: how does the image checksum get computed initially?
  Typically the build process computes and appends the checksum, so that the .elf or .dfu or .bin file has the signature built in.
  With CRC32 we don’t need to know more that the size of the region to be verified; if you stuff the right value at the very end, the CRC32 of the entire region is an invariant, and the bootloader just checks the invariant.

## Slide 9: There are many approaches…
Cryptographic signing means that the boot loader confirms that whoever “signed” the image knew certain secrets and possibly additional facts.
  Secret: some root key
  Additional facts: e.g. the hw serial number of the target device.
You can confirm that the image is approved and hasn’t been tampered with
We’re not going to tie the image to a given piece of hardware
Secure boot is a “good thing”

## Slide 10: Compromise is necessary
We need a boot loader quickly.
The secure aspects of this are mostly about signature etc.
We don’t have a great place to store secrets on our current platforms
So let’s say, for now, that we’ll try to detect corruption/validity without using secrets.
So we’ll also need some kind of metadata in the image that lets us check:
  Image is valid for this unit.
The boot loader therefore has to know what images are valid for this platform
We have a table of info that production is putting into high flash – we can use that as one input to the boot loader’s decision.

## Slide 11: More assumptions
We don’t want much variation in boot loaders (ideally all boot loaders for a given product family are the same)
  But some variation may be unavoidable.
  Use standard MCCI techniques to avoid conditional compiles.
Boot loader is written in C (or C++ if it turns out to be better/faster dev to do so)

## Slide 12: More assumptions
We always need to have a valid image in the storage element, in case we need to revert.
This means we have to have room for at least two images (the old one plus the new one)
We might generalize this, depending on how much work we can do in the boot loader.
But in any case, once we more than one images, we need a way to choose between them
And initially, we’ll have zero… need to deal with that
And sometimes we’ll have only one.

## Slide 13: More assumptions
The “program entry point” will either be &image[0], or else a pointer in a known location.

## Slide 14: Boot process (slow/thorough)
Self-check the boot loader
  What do we do if failure??? Flash light?
Two variables:
  Bool fProgramValid
  int iBestStoredImage; < 0  no stored image is valid, otherwise designates the stored image to be used.
  Bool fProgramMatches;
Check the image that’s currently in program flash
  If no good, set fProgramValid = false, otherwise true. (Comment: If fProgramValid is false, we always must try to load the “best” image from the SPI flash. If fProgramValid is true, we still might want to update, if the “best” image in SPI flash is “better” than the current program image.)
Initialize storage driver
  If this fails, set iBestStoredImage = -1, and skip down to [start-user-prog]
Find “best image” in storage (most recent confirmed image that is acceptable) [i.e. “while (iBestStoredImage < 0)..”
  Find the “most recent” image
  Validate it (and compare to current program image if fProgramValid is true; update fProgram)
  If not valid, find a previous image…
  If valid, set iBestStoredImage = index of this image.
Cases:
  ! fProgramValid && iBestStoredImage < 0:
    If must-update and no-valid image, then … problem … flash a light?
  fProgramValid && iBestStoredImage < 0
    If no-valid-image, skip to start-user-prog
  iBestStoredImage >= 0 && !(fProgramValid && fProgramMatches)
    Copy selected image to program storage
    Start-user-prog
  iBestStoredImage >= 0 && fProgramValue && fProgramMatches
    Start-user-prog
If verify fails, then .. Problem .. Need some policy on what to do (just loop forever until battery fails? Use NVIC_reset to reboot? Need some kind of diagnostic pattern on the LED.
Start-user-prog: go to entry point of program storage

## Slide 15: Flash organization
View flash as an array of fixed-size large blocks
  Some data structures in known places in large blocks
Header block would be nice, but maybe we can use the large block header for that.
Block size depends to some degree on the SOC chip and on the flash block size
STM32L0: 192k flash, so block should be “around” 192k

## Slide 16: Questions & puzzlers
We don’t need a directed “please load *this* image”, do we? Or do we need a GUID or similar for the “name” of the image, with the boot loader
  In that case, the flash image structure would be:
    Image: kind ‘A’
      Instance n
      Instance n+1
      Etc.
    Image: kind ‘B’
      …
    Perhaps “File system: kind” as another kind of thing; this would let us put user files on the flash using FATFS or similar.
  For the program flash, we’d need to know “kind” and “instance”
  When storing a new version, need an algorithm for choosing instance.

## Slide 17: Possible flash layout
Block allocation
  Option 1: Divide flash into “program-mem-size” blocks. For STM32L0, that would be 192k. 1MB / 192kB is 5 blocks, 2MB / 192kB is 10 blocks.
    In order to handle keeping a backup, we would need to have at least 2 blocks == 384 kB. But that would probably be enough.
  Option 2: Divide flash into 64kB chunks. Implies slightly more complex management, but it’s more efficient, especially if some of the flash is reserved for other things.
We also need to worry about storing the LoRaWAN error syndrome blocks; this can be

## Slide 18: SPI flash characteristics
We use 1M SPI on some boards, 2M on others
  4470: AT25SF081 (4k, 32k, 64k)
  1M on 4610, 4618, 4801: MX25R8035FZU1 / H1: 4k, 32k, 64k
  2M MX25R1635FZU0IH0: 4k, 32k, 64k
If we use 64k blocks, this fits 192k nicely (192k = 3 * 64k). We can’t use all of 192k because of the boot loader, so .. We have room left over for metadata.

## Slide 19: Image layout
Balance reliability against flexibility, so must take into account constraints from device.
Sector = 4k
Erase state == device is all 1s.
SPI flash allows changing single bits from 1>0, but 0>1 is only possible on a group basis (“erase”)
Image block = 192/4 = 48 sectors.
One approach
  Sector 0..n-1: headers
  Sectors n..47: data
When writing, erase the entire block. Then write data (sectors n..47). A blank header (sector 0) means “not valid” so we’re safe while writing.
Header can be as small as 256 bytes, because that’s the write quantum. Incremental programming is more complex. So we can be sure to write 256 bytes at a time.
Fundamental problem: want to ensure we can turn off power *at any time* and still have consistent state after reboot.
Fundamental strategy for reliable writes:
  When writing data is complete, write headers to confirm. If we know we’re starting from erased, we can write the metadata *twice*. (This may give protection against power-failure while writing first. If first != second on read, we say “not valid”).
  When reading data, check headers. If invalid, treat entire block as invalid.
  Always erase a block before writing.
Erase is tricky: it takes a long time. Power failure in mid erase leaves memory contents non-deterministic.
  So we need to deterministically mark data as erased before starting erase.
Zeroing header prior to erase is best idea.
In theory, we don’t need two headers; as long as the CRC can detect “enough errors” and we do careful validity checks, we are not likely to get fooled.
Issues of test…

## Slide 20: How to test
You can’t really test with real hardware – interesting cases are end of life, and not reproducible.
So we need a simulator.
  Should simulate SPI flash
  Should simulate NOR flash (harder because we don’t know error conditions, but we can ask ST)
  We can run on Linux with x86 CPU
We’d be testing corner cases with various injected faults. Don’t need to actually check anything other than the flash manipulation algorigthms.
  Test cutting power in middle of NOR flash programming – abort program, and then see if state of NOR flash is recoverable. Since bootloader is not affected by app programming, again we don’t need to do ARM emulation, so this can be just C/C++ on Linux or Windows or whatever.
Can test writer this way, too… only need SPI flash for that.

## Slide 21: Read algorithm in boot loader
No need to write.
Need SPI driver to read using READ command
Can copy code from Catena Arduino Platform but simplify.
SPI driver can be recoded from HAL and simplified. SPI frequency can be up to 33 MHz.
For 4801, we need to turn on power to the flash (Arduino D10, or PH1, and delay)

## Slide 22: Question: one bootloader image?
STM32L082 is different than SAMD21 etc.
  Probably different image
4801 is different than 4610
  Could be table driven, or could be different image
  Still need different values in table, but we do have the manufacturing data page.

## Slide 23: Checking an image
Input: vImageBase – base address of image in flash
Logic: block begins with space for nHeader headers; writer puts headers sequentially from 0. We read the *last* slot first, and keep backing up until we find a slot with a valid header.
Steps:
  1. iHeader = (nHeader – 1) * headerSize
  2. assert nHeader % 2 == 0. If iHeader < 0, done.
  3. read header from vImageBase + iHeader
  4. if header is “invalid”, try iHeader – (2 * headerSize).
  5. compare header to vImageBase + iHeader - headerSize
    If not equal, try iHeader – (2 * headerSize)
At this point, if iHeader < 0, we didn’t’ find a valid header at vImageBase
Otherwise we found one, and the data in the header structure is valid.
Only need a lot of headers if writing incrementally.
So we can say “4 header blocks” – if each block is 256x2 bytes, then that’s only 2k overhead.

## Slide 24: Schematic of block structure
h0
h1
h[n-1]
h2
data
…
Writing from 0 to n-1
Reading from n-1 to 0
Described by h[i such that i == max valid header index]

## Slide 25: Header structure
Offset | Name | Type/Size | Description
0 | uTag | uint32_t / 4 bytes | Magic number for any header.
4 | uRegionSize | uint32_t / 4 bytes | Size of region. Normally 192k (196,608)
8 | bReserved8[8] | uint8_t[8] / 8 bytes | Reserved for future use.
16 | Guid | uint8_t[16] / 16 bytes | GUID identifying the meta-contents of this block.
32 | Guid-Specific Data | uint8_t[252-32] == 220 bytes | Contents are GUID specific.
252 | Crc32 | uint8_t[4] | The CRC32 adjustment == crc32 of bytes[0..251], complemented, reversed, so that the CRC of the 256-byte buffer == the invariant. See https://en.wikipedia.org/wiki/Ethernet_frame#Frame_check_sequence

## Slide 26: Header for linear flash images
Offset | Name | Type/Size | Description
0 | uTag | uint32_t / 4 bytes | Magic number for any header.
4 | uRegionSize | uint32_t / 4 bytes | Size of region. Normally 192k (196,608)
8 | bReserved8[8] | uint8_t[8] / 8 bytes | Reserved for future use.
16 | Guid | uint8_t[16] / 16 bytes | GUID saying what this is: {3feb06e2-7180-4482-845a-b75de12388de} for linear flash image.
32 | ImageId | uint8_t[16] == 16 bytes | GUID identifying this image – different for each image
48 | uSequence | uint32_t == 4 bytes | Sequence number for this image
52 | … |  | TBD
252 | Crc32 | uint8_t[4] | The CRC

## Slide 27: Abstract boot loader
SPI flash a database of images and other things
Theres some stuff to make sure the bootloader is able to believe it. Then bootloader considers the images.
Bootloader needs to make a decision, based on the image it finds in nor flash, and the images it finds in spi flash, and any instructions that have been left for it administratively, what it should do?
  Copy image X to NOR flash, then start NOR flash (if NOR flash matches, just start NOR flash)
  Do nothing and start NOR flash
  (Discover a problem and copy a safe image to NOR flash)
  Do nothing and go to safe state
How does bootloader know which image is desired? Possibilities:
  SPI flash (special record that says “this one” – or look for the most recent version, etc.)
  EEPROM in the CPU
  FRAM
Easiest thing to describe is something in EEPROM that specifies the GUID of the image to run. Then the bootloader enforces the invariant that the application image in nor flash is the “best available” image of the images available before starting.

## Slide 28: Working with Flash in bootloader
We have 20k bytes of RAM on SM32L0

## Slide 29: Build process
Linker
Objdump (existing) converts to binary form to be loaded
Binary of image for flash
.elf
Post processor (new) (adds signature to be checked by boot loader)
Image to be loaded
Dfu prep (adds a little extra info needed for DFU processing)
.dfu file

## Slide 30: Things we have to be able to build
The boot loader itself
  Different .ld script – reserve the space used by application and mfg data
  No startup code, no HAL, etc. Everything will have to be as tight as possible. Debug only via STLINK; no debug prints, etc.
  Would be nice to have a common library used by multiple BSPs, so we avoid multiple bootloaders that have to be updated. But.. This complicates matters.
Images to be loaded by the boot loader (default)
  New .ld script
    Very much like current, but reserve the space used by the boot loader and mfg data
    This will have to be different for each MCU model we support because of differences in memory layout (STM32 families vary)
  Startup code already uses code from linker so it probably can be used as is.
  Different link command
?? Do we need to support the older way of doing things (it could be a variant of the boot loader build)
  Current .ld script

## Slide 31: Practical considerations
The signature check is going to change bootup time, even if we pass.
  This means that tricks like the Adafruit “double reset” for the boot loader might not work the same way.
  Maybe no problem.